## Slide 1: Wind Energy Conversion Systems
Muhammad Shamaas
2018-MS-EE-4

## Slide 2: Wind Energy Resource
The Site Wind Speed can be modeled by Weibull distribution. The Average Wind Speed increases with the Weibull distribution Scale Factor c and Shape Factor k.

## Slide 3: Wind Energy Resource
The Mean Wind Power Density and The Most Optimal Wind Speed increase with the Scale Factor c, but they decrease with the Shape Factor k.

## Slide 4: WECS Technology
Horizontal Axis Wind Turbine Energy Conversion Chain consists of:
Aerodynamic Subsystem (Turbine Rotor and Turbine Hub)
Drive Train (Low-speed shaft, Speed Multiplier and High-speed shaft)
Electromagnetic Subsystem (Electric Generator)
Electric Subsystem (Elements for Grid Connection)

## Slide 5: Wind Turbine Aerodynamics
The Power extracted from air mass by Energy Extracting Actuator Disc is:
Where Power Coefficient Cp is:
Example: Kite.

## Slide 6: Wind Turbine Aerodynamics
Tip Speed Ratio λ is:
Power Coefficient Cp(λ) performance curve shows that the Maximum value of Cp occurs at. It is lower than the Betz limit (Cpmax = 0.59).

## Slide 7: Power Generation System
Fixed-speed WECS:
General structure of a fixed-speed WECS (Squirrel Cage Induction Generator)
General structure of a limited variable-speed WECS (Wound Rotor Induction Generator)

## Slide 8: Power Generation System
Variable-speed WECS:
General structure of an improved variable-speed WECS (Doubly Fed Induction Generator)
General structure of a full variable-speed WECS (Squirrel Cage Induction Generator or Synchronous Generator)

## Slide 9: Wind Turbine Generators in Hybrid Power Systems
AC-coupled hybrid generation system:
Generators (Wind Turbine Generator, Diesel Power Plant)
AC Bus
Energy Storage (Accumulator, Flywheel)
Loads
Control System

## Slide 10: Wind Turbine Generators in Hybrid Power Systems
DC-coupled hybrid generation system:
Generators (Wind Turbine Generator, Diesel Power Plant, Photovoltaic Cells)
DC Bus
AC Filter
Energy Storage (Accumulator)
Loads
Control System

## Slide 11: Control Objectives
Aerodynamic power control through pitch/ stall control
Variable-speed operation and energy capture maximization, by means of generator control.
Grid Power Transfer Control, through the power electronics converter.