## Slide 1: Thermoelectric Effect
Muhammad Shamaas
2018-MS-EE-4

## Slide 2: Thermoelectric Effect
Thermoelectric effect is the direct conversion of temperature differences to electric voltage and vice versa using a thermoelectric device.
It encompasses three separately identified effects:
  Seebeck effect
  Peltier effect
  Thomson effect.

## Slide 3: Seebeck Effect
Seebeck Effect explains the conversion of heat directly into electricity at the junction of different types of conductors.
  = Seebeck Coefficient
  = Temperature Gradient

## Slide 4: Thermoelectric Generators (Seebeck Effect)
Thermoelectric generators are compact, expensive, inefficient and have no moving parts.
Power Recycling: Used in power plants for converting waste heat into additional electrical power.
ATEG: Automotive thermoelectric generators increase fuel efficiency by reusing waste heat.
Space probes: Radioisotopes are used in thermoelectric generators for heating.
Devices: Stove fans, body-heat powered lighting and smart watch, thermocouples, thermopiles and thermogalvanic cells.

## Slide 5: Peltier Effect
Peltier Effect explains the presence of heating or cooling at an electrified junction of two different conductors.
  = Thermal Energy Produced
  = Current
  = = Peltier Coefficient
  of Medium

## Slide 6: Thomson Effect
Thomson Effect describes the heating or cooling of a current-carrying conductor with a temperature gradient.
  = Heat Produced
  =Thomson Coefficient
  =Current Density
  =Temperature Gradient
It is a continuous version of the Peltier effect to account for a change in Seebeck coefficient with temperature.

## Slide 7: Thermoelectric Cooling (Peltier Effect)
Thermoelectric refrigerators: They are compact, have no circulating fluid or moving parts.
Thermal cyclers: Polymerase chain reaction (PCR) requires the precise, cyclic heating and cooling of samples to specified temperatures using Thermoelectric Coolers.

## Slide 8: Manufacturing Thermoelectric devices
Material | Seebeck Coefficient
Selenium | 900
Tellurium | 500
Silicon | 440
Germanium | 330
Nickel | -15
Constantan | -35
Bismuth | -72
40mm X 40mm
12V, 60W Generator

## Slide 10: Challenges
Inefficient: Currently, ATEGs are about 5% efficient. To compete with current power generation methods, it must possess
  greater than 3. However, over past five decades the room temperature ZT of materials with best available technology has only slightly increased from 0.6 to about 1.0.
Costly: The cost of Thermoelectric materials like half heuslers, skutterudites, bismuth telluride and lead telluride has discouraged large-scale manufacturing.

## Slide 11: Future of Thermoelectric Devices
Utilization of waste heat: Replacing the conventional electric generator with ATEGs means that the engine burns less fuel and releases fewer emissions. This could increase the fuel economy by up to 4%.
Hi-Z Inc. ATEG: The Generator produced 1 kW from a diesel truck exhaust system.
Advancements in thin-film and quantum well technologies: Low-cost production of tetrahedrite by Michigan State University, could increase efficiency up to 15% in the future.
Same efficiency at all power levels: More efficient than heat engines for low power applications (< 1kW).